## Slide 1: SPRO1 Task 2: Programming

## Slide 2: Little Primer – as you will work in the mechatronics lab

## Slide 3: Consequences of electrical Shock

## Slide 4: Guidelines
Always work with more people (never alone)
Use correct wires and probes
Wires and probes are connected without any electric source turned on
Modification of setup happens only without any electric source turned on
No food or drinking in the lab
Keep the lab tidy/clean up after yourselves

## Slide 5: Embedded Programming
Connect the Arduino Nano Pins to the other boards
  Check the pin descriptions and pinout
  Pin layout can be found by searching for Arduino Nano and ATMega328p
  Program the Arduino Nano in standard C language
You can use Laptop USB for Arduino Power Supply
Motor Power Supply – use Lab supply (Powerbank is also ok)

## Slide 6: Programming – how to start
Install Arduino Software – can be Microchip Studio or Visual Studio Code as in Embedded 1.
Microchip Studio – one option
Visual Studio Code – another option

## Slide 7
These files are part of your project
We are working on the main file.
Leave #define and #include as they are
Here you can set global variables. E.g. a pwm variable
The main function. Here your program starts executing
The green text, including ”//”, are comments.
This is free text and not compiled
Functions to enable you to use printf to communicate with PC or display
Visual Studio Code Example

## Slide 8: Platformio.ini
The build flags enable floating values when printing, using unsigned char by default and other things (the unsigned char is important for the display communication with the Nextion)

## Slide 9
We just want to count seconds. Create a global variable for that
Small Example Code
#define F_CPU 16000000UL //needs to be defined for the delay functions to work.
#include <avr/io.h> //used for pins input/output
#include <util/delay.h> //here the delay functions are found
#include <stdio.h> //used for printf function.
#include "usart.h"//for uart output to pc. Debugging purposes
//Declare global variables etc. here
unsigned int seconds_counter = 0;
//Declare function prototypes here
void increase_seconds_counter(void);
int main(void)
{
uart_init();//initialize communication with PC - debugging
io_redirect();//redirect printf function to uart, so text will be shown on PC or Nextion Screen
while(1)
{
//Put code in here
printf("The program has been running for %d seconds\n", seconds_counter);
_delay_ms(1000);
increase_seconds_counter();
}
return 0;
}
//Put in function implementations here
void increase_seconds_counter(void)
{
seconds_counter = seconds_counter + 1;
}
We want a special function to do it for us. Tell the compiler to look for the function later
Send this text to the PC. More on printf on the next slide
Wait 1000 ms
Call function to increase the seconds counter
Here we write the actual function operations
Increase global variable by one

## Slide 10: Printf – sending text to PC
printf("The program has been running for %d seconds\n", seconds_counter);
Function with arguments/parameters. Format is: printf(string, parameter1, parameter2,…)
String we want to send, including special indicators
%d: special indicator for ”decimal”. This converts value of first parameter to a text and inserts here
Character for new line: \n
Note: printf also has specifiers for floating point numbers. We do not need it in the project, but Alin can tell you about it. It also requires some extra setup for the project as seen on the previous slide
IMPORTANT: The Baud Rate set up on the PC and the one on the Arduino have to be the same, otherwise it will not work! The same accounts for the Nextion Display when communicating with that

## Slide 11: Compiling
Visual Studio Code: Compiling and deploying is done on the lower bar (checkmark and arrow)

## Slide 12: Result
There is a built-in serial monitor
  Play around with the code above.
  You can copy paste this into the provided, empty, sample project and move on from there

## Slide 13: Arduino Pin layout
Orange indicators denote names of PINS as in datasheet
Magenta, Green, and yellow indicators denote alternate pin functions – more details later
Cyan and White indicators denote Arduino-specific names – we do not use these, but they are the ones indicated on the board

## Slide 14: Overall tasks
Connection tasks:
  Connect optocoupler to Arduino using PB0 to D0 output
  Connect Arduino pin driver to L298 PD5 or PD6
  Connect Display to UART ports
Programming tasks:
  Enable Communication to Nextion LCD display
    You should use the debug functionality of the LCD display software as well.
  Enable Communication PWM output to control motor speed
  Enable reading and timing with optocoupler board
  Read voltage from ADC0 (PC0)
Overall:
  Get motor to run and be able to program it to different speeds (not specified)
  Measure the rotational speed using the optocoupler and encoder wheel from mechanical tasks.
  Display the speed at the Nextion LCD screen
  Display the measured voltage level on Nextion LCD screen

## Slide 15: Specific Tasks
Individual tasks
  Display two numbers on the Nextion Display using UART communication. One number should be integer and one should include decimal places. Start on the Nextion debugger, but should be on the display at the end
  Read an integer number from the Nextion Display using UART communication. Start on the Nextion debugger, but should be on the display at the end (same as 1)
  Measure time between two encoder wheel holes using the optocoupler. For this task, the resulting time can be sent to usual terminal.
  Setup and read voltage on ADC0 (PC0) pin. This will measure battery voltage later, for now any voltage between 0 and 5 V is ok. Display on terminal is ok
  Setup a PWM output on PD5 or PD6. Set up a desired frequency and a duty cycle of 20%. Connect to L298 module and observe changing motor speed
  Detect a button press from the Nextion display, indicating to start the programm (i.e. make a ”start” button on the display and execute other tasks after this, for example measuring and displaying motor speed)
  Combine the other results to display speed on display
  (BSc of 8 members only) Measure analog voltage in, and determine the time between two voltage pulses when the voltage goes from 0 to 3.3 volts
    Only BSc will use point 8 in the project period

## Slide 16: Signals, Pins, voltages – how does this work?
Select voltage levels commonly used:
  24 V, 12 V, 5 V, 3.3 V
In digital signals, we use those voltage levels for communication. Either a pin has 5 V on it or 0 V (ground, GND)
  If there is 5 V on it: Digital 1
  If there is 0 V on it: Digital 0
For programming there are predefined variables:
  DDRx sets the data direction (0=input / 1=output)
  PORTx sets port value: high/low if output
  PORTx enables internal pull-ups if input
DDRD = 0xFF;//Digital 0b11111111
PORTD = 0xF0;//Digital 0b11110000
Example:

## Slide 17: Optocoupler
Look at the pin descriptions on the board:
  VCC: Supply voltage. Connect this to 5 V from Arduino – here blue indicator (usually red)
  GND: Ground. Connect to GND pin from Arduino – here black indicator
  DO: Digital Out – connect this to PB0 – here red indicator due to multimeter in the sketch
  AO: Analogue out – leave open.
There is an LED on the board to indicate whether the optocoupler is open or blocked
  Could be used for debugging

## Slide 18: Optocoupler
Coding: PB0 has a special function if set up:
  Can copy a counter value into a register when it changes from 0V to 5V or from 5V to 0V
  Therefore, ideal to measure time difference between occurring holes

## Slide 19: Pins and special functions in embedded
Pins usually can have multiple functions – see datasheet. The different ports and alternative functions can be found:
  PB: Page 65
  PC: Page 68
  PD: Page 70
Small task:
  We will need a function called ICP1 – which PIN will we have to use? Hint: can be found on this slide

## Slide 20
There are also internal functions that operate ”in the background” once they are activated. We will need these three:
  Analog to Digital Converter (ADC)
  Timer/Counter 0 for PWM operation
  Timer/Counter 1 to measure time
How to set up: Special function registers
  Predefined registers you can read to and write from
  Generally bit-wise!
  Find in datasheet
Example: if we want ”normal mode of operation” and ”normal port operation”, what values to write in TCCR1A?
From datasheet page 108 and 109
TCCR1A = 0x00;

## Slide 21
What about register TCCR1B
We would like to enable a noise canceler on the input pin
We would like to a positive edge to trigger a capture event
We would like a prescaler of 1024
Questions:
  Which bits do we want to set to 1?
  With a prescaler of 1024 and a crystal giving clock of 16MHz, how much time does one count amount to?
TCCR1B = (1 << ICNC1) | (1 << ICES1) | (1 << CS12) | (1 << CS10);

## Slide 22: What happens with that timer/counter setup?
Counter starts in the background.
  Increases by 1 every 1024/16000000 seconds (64 microseconds)
  The increase happens no matter what the code is doing, so it is not disturbed
  Can count to max two bytes, i.e. 65535
If a rising edge (change from 0V to 5V) is detected on PB0/ICP1 it copies the current counter value into special register ICR1. This value can be read later. Note that these are in principle two 8-byte registers, but the compiler will take care of that for us
//Setup timer/counter 1 as pure ticks counter, counting //clock ticks with 1024 prescaling; i.e. no interrupts
TCCR1A = 0x00;
TCCR1B = 0xC5; //Input capture on positive edge ICP1 pin (PB0). Filter is //enabled. 1024 clock prescaler
DDRB &= ~0x01;//PINB0 as input for ICP1 use
PORTB |= 0x01;//Enable pullup

## Slide 23: Which strategy and registers to use for optocoupler?
You will need the following registers for the optocoupler challenge:
  TCCR1A - configuration
  TCCR1B – configuration
  DDRB + PORTB – as seen above: PB0 should be an input with a pull-up enabled
  TIFR1: ICF1 field in this register indicates that a rising edge on ICP1/PB0 has been detected. Fields needs to be writting high to reset
  TCNT1 - actual counter value. Set to zero on each detected edge
  ICR1 – value copied from TCNT1 on rising edge
Pages 108 to 113 in datasheet
Wait for ICF1 field to become 1
Reset TCNT1 and ICF1 field
Copy ICR1 variable into local variable
Display/send measured counts to Computer or Display
Initialize:
TCCR1A
TCCR1B
DDRB+PORTB
TCNT1=0

## Slide 24: How does the Motor and PWM work?
What is a PWM signal?
  Repeated signal either on or off (periodic)
  Has a base frequency and duty cycle
  Duty cycle between 0% and 100%
    In practice certain percentages can be difficult to obtain in more advanced circuits – here it should be no problem
  Combined with a filter (which a motor essentially is), a PWM can be regarded as an effective DC voltage.
  Also used for controlling light intensity of LEDs (effective – our eyes are the “filter” here)
PWM has to be applied to an H-bridge to drive the motor
Three PWM signals: 25, 50 and 75%

## Slide 25: Motor and Motor Driver
Amplifier: The Arduino cannot run a motor
Logic to the left can drive up to two DC motors – we only need one here.
Diagram explanations:
  small circles in front of AND gates denote inversion
  AND gates are the semi-round symbols. Both inputs high means output high
  FET Transistors (K-shaped with arrows). Behave like switches: Switch on if input high, else off.
Example: if
  EnB is high (5V)
  In4 is high (5V)
  In 3 is low (0V)
Then
  Output 3 is high
  Output 4 is low
Motor direction can be switched
We can generate PWM by switching EnB on/off really fast
From L298N data sheet

## Slide 26: Motor and Motor Driver
Connections if we use Output B:
  EnB 1 connect to PD6 (or PD5, can also be used)
  In4 connect to 5V from Arduino
  In3 connect to GND from Arduino
  Remove Connector 5 (CON5)
  +5V connect to 5V from Arduino
  GND connect to GND from Arduino
  +12V connect to power supply/battery
  Out3 and Out4: connect to motor terminals
Notice: it may make sense to create an external board with a couple of GND and 5V connectors, so it is easier to connect the above.
Notice: This is the setup where we use the Arduino as 5V source. Later we will have our own 5V supply, then we connect 5V to that
Whether or not to use the 5V regulator in the motor driver is up to you - but it is most feasible not to, as we will get a more powerful one later – and please do not use two different ones, as there might be slight differences (4.95V vs 5.05 for example), and connecting those is not good.
The 2025 version is not red, but green! Otherwise the same

## Slide 27: Motor and Motor Driver
If count >255
Set count = 0
Count = count + 1
If count > OCR0A set PWM pin to 5V
Else set PWM pin to 0V
How do we generate a PWM from Arduino?
  Timers have functions to do that – they will toggle a pin based on a specific count
  We will use timer/counter 0.
  Once set up like timer 1 (just with different registers, and only 8 bit counting) it runs in background
  Change in Duty Cycle is done by changing register OCR0A
PWM pin here are PD5 and PD6. Must be set up as output.
Principle of PWM generation. Runs in Background, you do not have to program this yourself
– you “just” have to set up the timer and update OCR0A

## Slide 28: Motor and Motor Driver
Registers of interest (pages 84-88 in datasheet):
  DDRD to set up output
  TCCR0A
    COM0A1 and COM0B1 should be set
    WGM01 and WGM00 should be set
  TCCR0B
    WGM02 should be cleared
    CS02 and CS00 should be set
  OCR0A
    At this counting value, the PWM pin is toggled
DDRD |=0x60;
//PWM Setup, see page 84 and following in datasheet for register description
TCCR0A |= 0xA3;//Fast PWM //mode with clear OC0A on compare match, set at bottom. Output B similar. //Page 84 and 86
TCCR0B |= 0x05;//1024 frequency scaling

## Slide 29: Analog to Digital conversion
Final purpose in this project:
  Measure battery voltage and warn if voltage is too low
Background:
  Battery voltage decreases when used
  We use a device to convert to 5V so we do not know the actual battery voltage (approx. 9V)
  Battery should not be discharged too much as this causes the voltage to become unstable
  Practically
  We use a voltage divider to reduce voltage to below 5V
  We use an Analog to Digital Converter (ADC) to measure the voltage

## Slide 30: Analog to Digital conversion
How does an ADC represent a voltage?
  It compares to a maximum voltage called reference voltage
  We use V
An ADC approximates the measured voltage as close as possible within the resolution, for example a 10 bit ADC:
  10 bits can represent integers, so from 0 to 1023
  The maximum voltage is represented by the biggest number, so 5V corresponds to 1023
  All other numbers fall in between (quantization), so 2.5V is approximated by 512
Different types of ADC
  Depends on speed. Most usual is successive approximation
  Takes some cycles to convert. Not an issue here

## Slide 31: Analog to Digital conversion
Register descriptions in Datasheet 217-220
  ADMUX – select which pin to measure on
  ADCSRB – Which mode. We want free running
    This means it is running in the background all the time and we just read off the latest result
  ADCSRA
    Enable the conversion, select input clock/prescaler
  ADCL and ADCH
    Converted voltage. Only lowest two bits of ADCH of interest along with all of ADCL. Always read ADCL first, so it is not safe to do this in a single operation
ADMUX = ADMUX | 0x40;//ADC0 single ended input on PortC0
ADCSRB = ADCSRB & (0xF8);//Free running mode
ADCSRA = ADCSRA | 0xE7; //Enable, Start conversion, slow input clock
unsigned int read_adc(void)
{
unsigned int adclow = ADCL;
return (adclow + ((ADCH & 0x03) << 8));//need to ensure that ADCL is //read first as it is not updated otherwise
}

## Slide 32: Nextion Display
Protocol with Serial communication and ASCII characters
Connect Blue and Yellow wire to PD0 and PD1
  We are using them as RX and TX pin of UART communication
  Connect Black wire to GND
  Connect Red wire to 5V
You can find online libraries for Arduino – Do not use them! They will confuse you. Doing this yourselves is not as hard as you think
Use Nextion Software to create a user interface
  For the debugger, sometimes you cannot see the whole window. This happens when your windows system has Zoom enabled – that will move parts of the window out of your screen. How will have to set screen zoom to 100%
Command set is found here:
  https://nextion.tech/instruction-set/
  You will mostly need variable setting like
    page0.n0.val=10
  In your C code it will look like
    printf("page0.n0.val=10%c%c%c", 255,255,255);
    The last three characters are flags and need to follow every command!
Connection from Arduino to display with nothing else connected

## Slide 33: Nextion Display
Flashing the Display
  Use the FTDI cable and connect as shown to the left
    Note, depending on version, blue and yellow cables might be swapped
  An extra connector board is used for this – backside shown lower right
  Make your own connector board.